## Slide 1
Evidence-Based Design for Safety and Quality
Roger S. Ulrich, Ph.D.
Center for Health Systems and Design
Colleges of Architecture and Medicine
Texas A&M University

## Slide 2
More evidence than expected: 900+ rigorous studies (Ulrich & Zimring, 2007)
A LOT of good evidence is available
Many designs make hospitals riskier for patients, families & staff
Full report: www.healthdesign.org/research/reports
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3
Surfaces commonly contaminated by MRSA
(Methicillin-resistant staphylococcus aureus)
R.S. Ulrich with P.A. Wilson

## Slide 4
Singles enable hospitals to separate patients upon admission, making it possible to prevent unrecognized carriers of pathogens from infecting others in multi-bed spaces
Why Single-Bed Rooms Reduce Infection Rates

## Slide 5
Problem: Unwashed Staff Hands
Low hand washing compliance has strong causal link with contact transmission of infection
  Compliance in busy units: 14-28%
  Education inadequate and transient

## Slide 6
Patient Bed
Alcohol-based gel dispenser
Automatic faucet (no touch)
Easy-to-clean basin counter (continuous impervious surface)
Design to Increase Hand Washing
Conveniently located basin in single room
Soap dispenser
M. D. Anderson Ambulatory Cancer Center
Houston
Handwash basins and hand rub dispensers should be close to staff movement paths, visually prominent, near care point

## Slide 7
Clarian West Medical Center Indianapolis
Design: HKS

## Slide 8
For busy preoccupied persons, out-of-sight may be out-of-mind

## Slide 9
STUDY: Effects of ICU Design on Handwashing
RESEARCH EXAMPLE
Study sites: two intensive care units (ICUs)--one older, one new--in a Texas hospital
Three types of patient rooms:
  Six-bed open bay
  Small single-bed rooms
  Large single-bed rooms with decentralized nursing stations
(Quan and Ulrich, in submission)
Centralized nurse stations
Notes: One research study looked at the infection rate of infants before and after they were moved to private rooms.

## Slide 10
Sinks and gel dispensers located close to staff work paths
New Intensive Care Unit
gel dispenser
sink
St. Joseph’s Medical Center, Bryan, TX
Design: WHR Architects

## Slide 11
0%
60%
50%
40%
30%
20%
10%
27%
38%
47%
28% increase
42% increase
74% total increase
Handwashing rate
Findings (Quan and Ulrich, 2006)

## Slide 12
Infection Rates in Old vs New ICUs
source: Quan and Ulrich, 2006
Reduced 44.4%
Move to new ICU with single rooms & better handwashing design
Old ICU

## Slide 13
Transfers Worsen Patient and Staff Safety
Increase infections
Transfers cause sharp peaks in medical errors
Major cause of staff injuries
Each transfer requires hours of staff time and paperwork
Each transfer adds .5 day to LOS

## Slide 14
Acuity-Adaptable, Single Coronary Critical Care Methodist Hospital, Indianapolis
BSA LifeStructures
Transfers reduced 90% compared to unit with multi-bed rooms
Saves $5 million per year
Medication errors reduced 70%
Pebble Project

## Slide 15: Annual Medication Error Index (errors/patient days) coronary critical care
More errors
Move to new unit with single, acuity-adaptable rooms
Source: A. Hendrich (2004). In Keeping Patients Safe: Transforming the Work Environment of Nurses. Quality Chasm Series, Institute of Medicine
Old unit with multi-bed rooms

## Slide 16
Most falls occur when patients get out of bed unassisted. Design for increasing assistance for patients and thereby reducing falls includes:
Problem: Falls
  Decentralized nurse stations
  Single-bed rooms designed to support family presence

## Slide 17
Acuity-Adaptable, Single Coronary Critical Care Methodist Hospital, Indianapolis
BSA LifeStructures
Pebble Project
Family Zone

## Slide 18
Design: BSA LifeStructures
Acuity-Adaptable, Family Centered CCU
Methodist Hospital, Indianapolis
Decentralized nurse stations improve observation of patients, safety

## Slide 19: Patient Fall Index (falls per 100 patient days)
Move to new unit with single family-centered rooms and decentralized nurse stations
More Falls
Source: A. Hendrich (2004). In Keeping Patients Safe: Transforming the Work Environment of Nurses. Quality Chasm Series, Institute of Medicine.
Old unit with multi-bed rooms, centralized nurse station

## Slide 20: Same-handed single patient room With evidence-based design (EBD) safety features
Large bathroom door
Direct path with hand assist to toilet
Handwashing sink with sight line
Dublin Methodist Hospital, Dublin Ohio
Design: Karlsberger with Cama
Sound-absorbing ceiling tile
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21
Same-handed single-bed rooms designed to increase patient safety
(UK hospital design proposal)