## Slide 1: Development of an Immersive Simulation Environment for the Study of IT impact in the Emergency Department
Presented by –
Li Lin, Ph.D.
Professor of Industrial and Systems Engineering
University at Buffalo, State University of New York
AHRQ Annual Conference - September 8, 2008
AHRQ Grant U18 HS16672-02 (Patient Safety and Simulation Research): Emergency Department Simulation for Research and Training in Health Care IT
Notes: <number>

## Slide 2: Background: ED Status Boards
Dry easel board (“whiteboard”) centrally located and publicly available to all ED staff
Information (with colors, symbols, stickers):
  Demographic
  Caregiver (physicians, RNs)
  Medical(symptoms, status, processes, & plans)
  Admission, discharge, transfers (ADT)
    Supports coordination, communication, workflow and tracking
Traditional whiteboards being replaced by computerized systems and displays
Impact of IT use to efficiency, quality of care, flexibility, communication, patient safety and staff workload remains to be studied
Notes: <number>

## Slide 3
Replaced with
Electronic patient tracking system
Manual patient tracking system

## Slide 4: Impact of IT Implementation
Technology replacements
  Rapidly designed into the system
  Consequences on patient care and safety
Important to understand impact of IT solution before implementation through testing & design
Simulation studies can help avert safety concerns with technology implementation and prevent adverse events due to technology use
Notes: <number>

## Slide 5: Motivation
IT solutions can bring financial benefits, but their impact to healthcare quality, efficiency and patient safety is issue for research
Need to study critical human behavioral processes and performance with technology limitations
Simulation can facilitate study of medical professionals’ behavior and performance in a controlled lab setting
Challenges in creating a realistic ED by simulation
  Operational and clinical realism
Notes: <number>

## Slide 6: Research Objectives
To develop a discrete-event simulation (of operational processes) based immersive experimental environment (i.e., the Patient Tracking System Simulator) that represents an ED white board
To test ED staff’s performance in a dynamic ED environment using IT (contrasting different workload and designs)
Participants: ED nurses and secretaries
Study to assess:
  Caregivers’ awareness
  Interruptions and distractions
  Recovery from system failures
  Response to critical events
Notes: <number>

## Slide 7: The Multi-disciplinary Research Team
University at Buffalo
  PI: Li Lin, Ph.D., Co-I: Ann Bisantz, Ph.D. (Department of Industrial & Systems Engineering)
  Co-I: Jennifer Brown, M.D. (Department of Emergency Medicine)
  Ph.D. students: Priya Pennathur and Dapeng Cao (Department of Industrial & Systems Engineering)
University of Rochester
  R. J. “Terry” Fairbanks, M.D.
University of Florida, Jacksonville
  Robert Wears, M.D.
  Shawna Perry, M.D. (now at Medical College of Virginia)
Meeting the challenges:
  Operational dynamics and situation awareness – industrial engineering and human factors
  Clinical realism – ED physicians
Notes: <number>

## Slide 8: Simulation Study
Notes: <number>

## Slide 9: Simulation for Design Support
Iterative user-centered design
Systematic investigation of key design parameters
Simulates realistic characteristics of emergency department (ED)
Helps evaluate usability and performance measures under no-risk lab conditions
Provides ED staff training in use of technologies under realistic ED conditions without compromising care and safety

## Slide 10: Discrete-event Simulation
  State-of-the-art computer software that mimics operational details of complex systems.
  Pac-Man-like animated simulation conveys reality in pictures.
  Consistently ranked as one of top methods for operations analysts and industrial engineers.
  Models in computer represent real operations and test them for performance under different conditions.
  Most useful in studying system performance - answer “WHAT IF’s” before investing and making changes.
  Widely used in manufacturing, transportation, service industries, and many other applications.

## Slide 11: Simulation of an ED

## Slide 12: Sample ED Discrete-event Simulation Results (1)
Utilization
%
Time

## Slide 13: Sample ED Discrete-event Simulation Results (2)
Time
Utilization
%
No. of Physicians

## Slide 14: Building the ED Patient Tracking System Simulator (PTSS)
Patient scripts
  Clinical information for simulated patients in the ED
  Pseudo patient names, age, gender, chief complaints, events and orders
  Chief complaints
    Severity based on hospital ED-DES
  Clinical progress information & Medical realism
    Scripted by physicians at relevant events
    Validation for medical realism
  Representing a patient record
Integrated into an ED Event Calendar with discrete time points for an immersive simulation experiment (simulated white board)

## Slide 15: Example Patient Script
Patient ID | Severity Type | Comments for ED-DES | Description of Events | Time
37 | 3 |  | Time of Arrival | 96.88
37 | 3 |  | Triage Start | 97.01
37 | 3 |  | Triage End | 99.06
37 | 3 | Resp Tx | Registration Start | 111.33
37 | 3 |  | Registration End | 117.47
Chief Complaint | First name | Last name | Age | Gender
Difficulty breathing | Helen | Waterman | 35 | F

## Slide 16: Example Event Calendar

## Slide 17: Patient Tracking System Simulator
Notes: <number>

## Slide 18: Study Design
Participants
  Charge nurses, secretaries from emergency department
  10 nurses, 10 secretaries
Display types
  Desktop, Large screen display
Demand levels (patient volume)
  Low, high
Two 2-hour sessions, 1 to 2 weeks apart
Each session
  2 scenarios with varying ED demand levels

## Slide 19: Tasks and Measures
Typical ED paperwork
Phone/pager prompts to mimic real ED tasks
Situation awareness measures
  Using Situation Awareness Global Assessment Technique (SAGAT, Endsley 1995)
Information probes
  Identifying information updates and deviations
System failures or “blanking out”
  Ability to respond, recover from failure
Audio and screen recording
  User-system interaction issues
Workload
  NASA-TLX (a subjective workload assessment technique
Experiments being completed, data analysis to begin

## Slide 20: Conclusions
Uniqueness of our study
  Not a mannequin simulator, but simulation of ED for assessing design issues in technology use
  Understanding interaction, human factors measures
  Immersive ED environment useful for staff training in technology use
Serves as a case of technology design for complex systems, within a controlled setting
Framework for use of ED simulation in future studies on IT design and use in healthcare
Multi-disciplinary team with industrial engineering and medical expertise in developing integrated solutions