## Slide 1: Technical Brief on particle beam radiotherapies for the treatment of cancer
T Trikalinos, T Terasawa, S Ip, G Raman, J Lau
Tufts EPC
Presenter: Tom Trikalinos, MD, PhD, Co-Director, Tufts EPC.
Notes: <number>

## Slide 2: Introduction (I)
Radiation therapy is pivotal in cancer treatment
Based on physics, there are 3 broad groups of external radiation therapy:
  Photons
  Electrons
  Charged particles (e.g., protons)
Notes: <number>

## Slide 3: Introduction (II)
Charged particle radiotherapy has been clinically available since 1954.
Appropriate clinical utilization is controversial.
  No documented superiority over radiotherapy alternatives in comparative data
  Expensive
Notes: <number>

## Slide 4: Technical Brief
Rapid report that describes:
The technology
Its availability, diffusion and cost
Type of facilities, provider training
State-of-science:
  Type of studies, participants, interventions, designs
  No focus on findings
Notes: Technical Briefs generally focus on interventions for which there are limited published data and too few completed protocol-driven studies to support definitive conclusions.
<number>

## Slide 5: Technical Brief Methods
Combination of general Internet searches
  Information on the technology, the principles it operates on, its availability, uptake and cost one has to search beyond the published literature
And systematic scan of the published literature
  Describe published research
Notes: <number>

## Slide 6: General Internet Searches
Google “particle beam therapy” and “proton beam therapy”
Visiting relevant links (first 10 pages)
Websites of radiotherapy organizations, treatment centers, manufacturers
FDA Center for Devices and Radiological Health; Manufacturer and User Facility Device Experience Database
Notes: <number>
By their very nature, some questions cannot be answered from the published literature. General Internet searches are necessary.

## Slide 7: Systematic literature scan (I)
MEDLINE searches to identify studies:
Charged particle radiotherapy performed
Cancer in >80% of patients
Any clinical outcome, any harm
Any design, ≥10 patients treated*
English, German, Italian, French, Japanese
Notes: <number>
* <10 considered for reporting of harms

## Slide 8: Systematic literature scan (II)
Descriptive statistics for designs, clinical and treatment characteristics, clinical outcomes and adverse events reported
We stratified results by cancer type
  (ocular, head and neck, spine, GI, prostate, bladder, uterus, bone and soft tissue, lung, breast, miscellaneous)
Notes: <number>

## Slide 9: Results

## Slide 10: Physics of charged particle versus photon radiotherapy
Photon radiotherapy
Uses ionizing photon (X- or γ-ray) beams for the locoregional treatment of disease
Radiation damage to DNA of healthy and tumor cells alike triggers complex reactions that ultimately result in cell death
Cellular damage increases with the (absorbed) radiation dose (measured in Gy)
Notes: <number>

## Slide 11: Depth-dose distribution of photons
Notes: <number>

## Slide 12: Particle beam radiotherapy
Uses charged particles (e.g., protons, helium ions, carbon ions)
Charged particles deposit most of their energy in the last millimeters of their trajectory (when their speed slows)
Sharp localized peak of dose (Bragg peak)
Notes: <number>

## Slide 13: A pristine Bragg peak (I)
Notes: <number>

## Slide 14: A pristine Bragg peak (II)
Notes: <number>
Lower intensity

## Slide 15: A pristine Bragg peak (III)
Notes: <number>
Lower energy (speed)

## Slide 16: Multiple Bragg peaks
Notes: <number>
Add 12 bragg peaks

## Slide 17: Spread-out Bragg peak (SOBP)
Notes: <number>
Add 2 bragg peaks

## Slide 18: Spread-out Bragg peak (SOBP)
Notes: <number>
Add 12 bragg peaks

## Slide 19: Photons vs SOBP

## Slide 20: Large facilities
January 2007
Architectural model
University of Pennsylvania (Perelman center for
Advanced Medicine)

## Slide 21: Practical information (I)
Institute | Particle | Maximum Clinical Energy (MeV) | Start | Patients treated | 
 |  |  |  | Number | Date of count
LLU, CA | proton | 250 | 1990 | 11414 | Nov-06
MPRI, IN | proton | 200 | 1993 | 379 | Dec-07
UCSF, CA | proton | 60 | 1994 | 920 | Mar-07
NPTC-MGH, MA | proton | 235 | 2001 | 2710 | Oct-07
MD Anderson, TX | proton | 250 | 2006 | 527 | Dec-07
FPTI, FL | proton | 230 | 2006 | 360 | Dec-07
Operating particle beam facilities in the US (2008)
Notes: <number>

## Slide 22
Institute | Now in constru-ction | Parti-cle | Maximum Clinical Energy (MeV) [Accelerator] | Treat-ment rooms | Gant-ries | Cost (mil-lion $) | Estima-ted start date
University of Pennsylvania, PA | Yes | proton | 230 [Cyclotron] | 5 | 4 | 140 | 2009
Hampton University, VA | Yes | proton | [?] | 5 | 4 | 225 | 2010
Northern Illinois Proton Treatment and Research Center, IL | No | proton | 250 [?] | 4 | 2 or 3 | 159 | 2010
Practical information (II)
Large particle beam facilities being planned/
constructed in the US (2008)
Notes: <number>

## Slide 23
Evidence maps
Notes: <number>

## Slide 24: Evidence maps
Notes: <number>

## Slide 25: Evidence maps: comparative studies
Notes: <number>

## Slide 26: Evidence maps: comparators
Comparison | RCTs (n=10) | Nonrandomized comparative (n=13) | Example
Particles vs particles | 4 | 1 | Higher vs lower proton dose for uveal melanoma
Particles only vs other Tx | 3 | 8 | Carbon-ion vs photon + brachytherapy for uterine cancer
Tx with particles vs other Tx without particles | 3 | 4 | Photon RT + proton boost vs photon RT + photon boost for prostate cancer
Notes: <number>

## Slide 27: Discussion (I)
The theoretical advantages of charged particle irradiation have not been demonstrated in comparative studies
  Claims of “higher effectiveness”
  Claims of “less toxicity”
vs what?
vs what?
In whom?
In whom?

## Slide 28: Discussion (II)
Some authorities see no need for RCTs
Superior dose distributions with charged particles vs photons
The biological effects of e.g. protons are similar to those of photons, and thus known
It is self evident that precise localization of dose is beneficial
This is a scarce (limited) resource. Use it in an optimal way (may not include RCTs)

## Slide 29: Discussion (III)
Even strong pathophysiological rationale can mislead
Many instances of clinical equipoise between charged particle radiation and other modalities, in rare and common cancers
Are any differences large enough to justify routine use?

## Slide 30: Discussion (IV)
For rare tumors near anatomically critical structures where extreme precision is sine qua non, relevant comparators are
  Intensity modulated radiation therapy
  Conformal radiation surgery

## Slide 31: Discussion (V)
For common cancers where “extreme” precision is currently not a mandate, relevant comparators are practically all currently used radiation modalities

## Slide 32: Recommendations for future research
Capitalize on existing data
  Reanalysis of existing individual patient data with optimal statistical methods
Generate comparative data, first for common cancers
  Evaluate patient-relevant outcomes
  RCTs
Conditional coverage with evidence development?

## Slide 33: Parting points
Tradeoff: high cost and limited availability against unclear effectiveness compared with contemporary alternatives
  Cost-effectiveness (-utility) RCTs?
Is pathophysiology and physics sufficient to justify diffusion to common cancers?
  Antiarrhythmics for premature ventricular contractions
  Erythropoetin for anemia in chronic kidney disease

## Slide 34: Hidden slides

## Slide 35: What does the result look like?

## Slide 36: Background on photon and particle beam radiotherapy
Notes: <number>
Unusually long

## Slide 37: Comparators in RCTs
Cancer type and center | Comparison | N | Survival [Overall/ specific]
Ocular (uveal melanoma) |  |  | 
MGH (USA) | Higher vs lower dose proton RT | 188 | No/No
UCSF (USA) | Helium RT vs I-125 brachytherapy | 136; 184 | Yes/Yes
Orsay (France) | Proton RT vs proton RT + laser TTT | 151 | Yes/Yes
Head/neck (skull base chordoma/chondrosarcoma) |  |  | 
MGH (USA) | Higher vs lower dose proton RT | 96 | Yes/No
Head/neck (brain glioblastoma) |  |  | 
UCSF (USA) | Higher vs lower dose proton RT | 15 | Yes/Yes
GI (pancreatic cancer) |  |  | 
UCSF (USA) | Helium RT vs photon RT | 49 | Yes/Yes
Prostate |  |  | 
MGH & LLU (USA) | Photon RT + standard dose proton vs Photon RT + high dose proton | 393 | Yes/Yes
MGH (USA) | Photon RT + local photon boost vs Photon RT + local proton boost | 202; 191 | Yes/Yes
GI: Gastrointestinal; RT: radiotherapy; TTT: transpupillary thermotherapy

## Slide 38
Cancer type and center | Comparison | N | Survival [Overall/ specific]
Ocular (uveal melanoma) |  |  | 
Orsay (France) 34 | Proton RT vs I-125 brachytherapy | 1272 | Yes/No
UCSF (USA)35 | Helium RT vs I-125 brachytherapy | 766 | No/No
MGH (USA)36 | Proton RT vs enucleation | 556 | Yes/Yes
UCSF (USA)33 | Helium RT vs I-125 brachytherapy | 426 | No/No
[Wilson 1999 - Unclear center]45 | Proton RT vs I-125 brachytherapy vs Ru-106 brachytherapy | 267 | Yes/No
MGH (USA)44 | Proton RT vs enucleation | 120 | Yes/Yes
UCSF (USA)37 | Proton RT vs proton RT + laser TTT | 56 | No/No
Head/neck (skull base adenocystic carcinoma) |  |  | 
HMI (Germany)43 | SFRT/IMRT vs SFRT/IMRT + proton boost | 63 | Yes/Yes

## Slide 39
Uterus |  |  | 
NIRS (Japan) | Carbon RT vs photon RT + brachytherapy | 49 | No/No
GI (Bile duct) |  |  | 
UCSF (USA)55 | Proton RT vs photon RT | 62 | Yes/Yes
UCSF (USA)42 | Surgery + photon RT vs Surgery + proton RT | 22 | No/No
Prostate |  |  | 
LLU (USA)39 | Watchful waiting vs surgery vs standalone photon RT vs photon RT + proton boost RT vs standalone proton RT | 185 | No/No
MGH (USA)38 | photon RT + photon boost vs photon RT + proton boost | 180 | Yes/Yes

## Slide 40: Technical Brief
AHRQ has asked Tufts EPC to perform a Technical Brief on the role of particle beam radiotherapies in the treatment of cancer conditions
A Technical Brief is a rapid report on an emerging clinical intervention that provides an overview of key issues. Technical Briefs generally focus on interventions for which there are limited published data and too few completed protocol-driven studies to support definitive conclusions.
Notes: <number>
The emphasis of the Technical Briefs is to provide an early objective description of the state of science, a potential framework for assessing the applications and implications of the new interventions, a summary of ongoing research, and information on future research needs.

## Slide 41: Key question 1
1.a. What are the different particle beam radiation therapies that have been proposed to be used on cancer?
1.b. What are the theoretical advantages and disadvantages of these therapies compared to other radiation therapies that are currently used for cancer treatment?
1.c. What are the potential safety issues and harms of the use of particle beam radiation therapy?
Notes: <number>

## Slide 42: Key Question 2
2.a. What instrumentation is needed for particle beam radiation and what is the Food and Drug Administration (FDA) status of this instrumentation?
2.b. What is an estimate of the number of hospitals that currently have the instrumentation or are planning to build instrumentation for these therapies in the USA?
2.c. What instrumentation technologies are in development?
Notes: <number>

## Slide 43: Key Question 3
Perform a systematic literature scan on studies on the use and safety of these therapies in cancer, with a synthesis of the following variables:
3.a. Type of cancer and patient eligibility criteria
3.b. Type of radiation, instrumentation and algorithms used
3.c. Study design and size
3.d. Comparator used in comparative studies.
3.e. Length of followup
3.f. Concurrent or prior treatments
3.g. Outcomes measured
3.h. Adverse events, harms and safety issues reported
Notes: <number>

## Slide 44: Schematic of a proton beam radiotherapy center
Ion source
Accelerator
(cyclotron)
Rotational gantries
Beam transportation
components
Fixed beam
Audrey Mahoney, Tufts MC EPC
Notes: <number>

## Slide 45: Evidence maps
Cancer type | Single arm | RCTs | Nonrandomized comparative | Total
Ocular | 80 | 4 | 7 | 91
Head/neck | 53 | 2 | 1 | 56
Spine | 9 | 0 | 0 | 9
GI | 18 | 1 | 2 | 21
Prostate | 14 | 3 | 2 | 19
Bladder | 3 | 0 | 0 | 3
Uterus | 4 | 0 | 1 | 5
Bone/soft tissue | 6 | 0 | 0 | 6
Lung | 17 | 0 | 0 | 17
Breast | 2 | 0 | 0 | 2
Miscellaneous | 14 | 0 | 0 | 14
Notes: <number>